## Slide 1: Introduction of Smart Structure Technology
Chul Min Yeum
Assistant Professor
Civil and Environmental Engineering
University of Waterloo, Canada
CIVE 497 – CIVE 700: Smart Structure Technology
Last updated: 2018-01-06

## Slide 2
Outlines
Part I: Introduction of Smart Structure Technology
Part II: Review of the Course Syllabus
Part III: Instructor's Prior Research

## Slide 3
Smart Structures and Systems
Data
Information
Sensing
Processing
Analyzing
Structure
Knowledge/ Decision
Human engineers
Automation
Notes: Doctor (i.e. pulse, temperature, color, ..)
Civil Engineer’s role
Who is going to treat the problem?

## Slide 4
Smart Sensing and Data Processing
Computing
Mobility
Sensing
Ultimately, we emulate the activities of civil engineers in a rapid and automated ways with high precision.
Notes: Civil Engineer’s actions relevant to civil engineering applications

## Slide 5
Definition of Structural Health Monitoring
Structural Health Monitoring is the process of implementing a damage detection strategy for aerospace, civil and mechanical engineering infrastructure.
The SHM process involves:
  The observation of a system over time using periodically sampled dynamic response measurements from an array of sensors.
  The extraction of damage-sensitive features from these measurements.
  The statistical analysis of these features is then used to determine the current state of system health.
Notes: Building a new thing vs Fixing an old one

## Slide 6
Motivations for Structural Health Monitoring
Local damage detection methods, referred to as Non-Destructive Evaluation (NDE), are well developed and widely used.
These methods have difficulty when large surface areas need to be inspected.
Need more global and automated damage detection methods.
Economic and life-safety advantage.
Move from time-based maintenance to condition-based maintenance.
New business models: Manufacturers of large capital investment hardware can charge by the amount of life used instead of a time-based lease.
Notes: Monitoring == Management

## Slide 7
Structural Health Monitoring (SHM) Process
Step 1: Define Damage
Step 2: Identify Damage
Step 3: Locate Damage
Step 4: Quantify Damage
Step 5: Predict Remaining life
Definition: SHM is a process to monitor and evaluate the safety and integrity of a structural system throughout its life span.
Notes: Rytter, A. (1993). Vibrational based inspection of civil engineering structures (Doctoral dissertation, Dept. of Building Technology and Structural Engineering, Aalborg University).

## Slide 8
Definition of “Damage”
Damage will be defined as changes to the material and/or geometric properties of a structural or mechanical system, including changes to the boundary conditions and system connectivity, that adversely affect the current or future performance of that system.
Examples:
  crack in mechanical part (stiffness change)
  scour of bridge pier (boundary condition change)
  loss of tire balancing weight (mass change)
  loosening of bolted joints (connectivity change)

## Slide 9
Smart Structures and Systems
Incorporating advanced technologies in the fields of
Non-destructive evaluation
Structural health monitoring
Structural assessment
Structural control
Smart structure materials
Construction management

## Slide 10
Smart Structures and Systems

## Slide 11
Passive and Active Sensors
Passive sensors are only used to detect energy when the naturally or artificially occurring energy is available.
Active sensors have its own energy source to interactive with objects.
Passive sensor
Active sensor
GPS
Camera
Accelerometer
Interac
Stethoscope
IR-camera
Smoke detector
Scanner
Ultrasound
Laser scanner
Camera + flash
X-ray
Measuring laser
Kinect
Thermometer
Thermometer
Notes: Sensors are used to measure a physical quantity.
The distinction between passive and active sensor characterize the sensor ability to retrieve a measurement without or with inputting energy (mechanic or electromagnetic or else) in the environment.

## Slide 12
Electromagnetic Spectrum
https://www.flickr.com/photos/advancedphotonsource/5940581568

## Slide 13
Mechanical Vibration
https://www.olympus-ims.com/en/ndt-tutorials/flaw-detection/ultrasound/

## Slide 14: Applications of Smart Structure Technology in Civil Engineering

## Slide 15
Structural Engineering: Wireless Monitoring of a Cable-Stayed Bridge
Cho, S., Jo, H., Jang, S., Park, J., Jung, H. J., Yun, C. B., ... & Seo, J. W. (2010). Structural health monitoring of a cable-stayed bridge using wireless smart sensor technology: data analyses. Smart Structures and Systems, 6(5-6), 461-480.
Notes: Low power consumption
Enough sensitivity
Syncronization

## Slide 16
Structural Engineering: Visual Inspection – Crack Detection
Jahanshahi, M. R., Masri, S. F., Padgett, C. W., & Sukhatme, G. S. (2013). An innovative methodology for detection and quantification of cracks through incorporation of depth perception. Machine vision and applications, 24(2), 227-241.

## Slide 17
Structural Engineering: Bridge Deck Assessment Robot
https://cait.rutgers.edu/rabit-asce-award

## Slide 18
Structural Engineering: Visual Inspection – Façade Inspection using UAVs
Choi, J., Yeum, C., Dyke, S., & Jahanshahi, M. (2018). Computer-aided approach for rapid post-event visual evaluation of a building façade. Sensors, 18(9), 3017.

## Slide 19
Structural Engineering: Visual Inspection – 3D Pavement Inspection
Jahanshahi, M. R., Jazizadeh, F., Masri, S. F., & Becerik-Gerber, B. (2013). Unsupervised Approach for Autonomous Pavement-Defect Detection and Quantification Using an Inexpensive Depth Sensor. Journal of Computing in Civil Engineering, 27(6), 743–754.

## Slide 20
Structural Engineering: Delamination Detection using Acoustic Analysis
https://go.unl.edu/ic7w
https://news.unl.edu/newsrooms/today/article/how-acoustics-can-be-an-early-warning-system-for-bridges/
https://www.youtube.com/watch?v=GPfPdk_t7gk
Notes: https://news.unl.edu/newsrooms/today/article/how-acoustics-can-be-an-early-warning-system-for-bridges/

## Slide 21
Structural Engineering: Acoustic Impact-Echo Investigation of Concrete Delamination
https://www.sciencedaily.com/releases/2012/10/121022162701.htm
Mazzeo, B. A., Patil, A. N., & Guthrie, W. S. (2012). Acoustic impact-echo investigation of concrete delaminations using liquid droplet excitation. NDT & E International, 51, 41–44. https://doi.org/10.1016/j.ndteint.2012.05.007

## Slide 22
Structural Engineering: Robotic for Structural Assessment
https://youtu.be/YCihWIBIGZ8

## Slide 23
Structural Engineering: Video Surveillance of Vehicle Clearance
https://www.youtube.com/yovo68
Notes: https://www.youtube.com/results?search_query=bridge+height+limit+monitoring

## Slide 24
Structural Engineering: Rail Inspection using Non-contact Ultrasonic Transducers
Rizzo, P., Cammarata, M., Bartoli, I., di Scalea, F. L., Salamone, S., Coccia, S., & Phillips, R. (2010). Ultrasonic guided waves-based monitoring of rail head: laboratory and field tests. Advances in Civil Engineering, 2010.
https://www.youtube.com/watch?v=wqKzrFeYEU8

## Slide 25
Structural Engineering: Coating Thickness Quantification using Laser Thermography
Hwang, S., Park, J., Jin, Z., & Sohn, H. Reference-free Coating Thickness Quantification using Laser Thermography under Various Exterior Temperature Conditions.

## Slide 26
Structural Engineering: Delamination Detection using Piezoelectric Sensors
Yeum, C. M., Sohn, H., & Ihn, J. B. (2011, March). Delamination detection in a composite plate using a dual piezoelectric transducer network. In Health Monitoring of Structural and Biological Systems 2011 (Vol. 7984, p. 798406).

## Slide 27
Structural Engineering: Autonomous Vehicle for Structural Control and Assessment
https://www.youtube.com/watch?v=TS2KWmGCsnQ

## Slide 28
Structural Engineering: Image Registration
Li, R., Yuan, Y., Zhang, W., & Yuan, Y. (2018). Unified Vision‐Based Methodology for Simultaneous Concrete Defect Detection and Geolocalization. Computer‐Aided Civil and Infrastructure Engineering.

## Slide 29
Material Engineering: Self-Healing Concrete
https://www.youtube.com/watch?v=eN-vJB7yeJI
Notes: https://www.youtube.com/watch?v=eN-vJB7yeJI

## Slide 30
Material Engineering: Shape Alloy
https://youtu.be/-K57cbOhA5g

## Slide 31
Construction Engineering: Automated construction state estimation
https://uwaterloo.ca/scholar/chaas/research
Notes: Aecon III NSERC CRD, OPG UNENE CRD, Discovery Grant, and scholarships
Relative transformations between designed and built objects and systems of objects for rigid and flexible cases
Continuous built status analysis and fabrication control

## Slide 32
Construction Engineering: Crane Camera Solution (Pix4D)
https://youtu.be/wZazAIiljKw

## Slide 33
Construction Engineering: Action Recognition in Construction Sites
Golparvar-Fard, M., Heydarian, A., & Niebles, J. C. (2013). Vision-based action recognition of earthmoving equipment using spatio-temporal features and support vector machine classifiers. Advanced Engineering Informatics, 27(4), 652–663.

## Slide 34
Construction Engineering: Craft Worker Health and Productivity Improvement
https://uwaterloo.ca/scholar/chaas/research

## Slide 35
Transportation Engineering: Autonomous Vehicle
https://youtu.be/xsQvq4WlUYU

## Slide 36
Earthquake Engineering: Social Media Data Analysis
Sakaki, T., Okazaki, M., & Matsuo, Y. (2013). Tweet Analysis for Real-Time Event Detection and Earthquake Reporting System Development. IEEE Transactions on Knowledge and Data Engineering, 25(4), 919–931.
Notes: https://ieeexplore.ieee.org/document/6152108/

## Slide 37
Earthquake Engineering: Post-Disaster Reconnaissance
Yeum, C. M., Dyke, S. J., Benes, B., Hacker, T., Ramirez, J., Lund, A., & Pujol, S. (2018). Postevent Reconnaissance Image Documentation Using Automated Classification. Journal of Performance of Constructed Facilities, 33(1), 04018103.
https://youtu.be/zNwoogoYQ7o

## Slide 38
Transportation Engineering: Vehicle Tracking / Counting
https://www.youtube.com/watch?v=_i4numqiv7Y&t=8s

## Slide 39
Transportation Engineering: License Plate Estimation
Notes: https://www.cs.mcgill.ca/~joerg/SEL/COMP-533_Handouts_files/407-ETR-final_design.pdf

## Slide 40
Transportation Engineering: Driver Distraction Monitoring
https://www.youtube.com/watch?v=ImAlBVLXiBA

## Slide 41
Environmental Engineering: Air Quality Monitoring (Breathe Cam)
https://www.cmu.edu/homepage/health/2014/fall/observable-air.shtml
https://www.youtube.com/watch?time_continue=1&v=rV21uP9XcFg

## Slide 42
Environmental Engineering: Visual Opacity of Fugitive Plumes
Du, Ke, et al. "Digital Optical Method to quantify the visual opacity of fugitive plumes." Atmospheric environment 77 (2013): 983-989.
https://youtu.be/tNse9hYYEBc
Notes: https://www.sciencedirect.com/science/article/pii/S135223101300472X#fig1

## Slide 43
Surveying: Photogrammetry
https://youtu.be/uZ5KIgQmJ9w

## Slide 44
Surveying: Mobile Mapping Solution
https://youtu.be/52x1N7U0EAk

## Slide 45
Surveying: GeoSLAM ZEB-REVO
GeoSLAM: All-in-one Mobile Scanning Device: https://youtu.be/czqVuoubADo

## Slide 46
Smart Structures and Systems
Data
Information
Sensing
Processing
Analyzing
Structure
Knowledge/ Decision
Human engineers
Automation