## Slide 1: Edge Detection
Chul Min Yeum
Assistant Professor
Civil and Environmental Engineering
University of Waterloo, Canada
CIVE 497 – CIVE 700: Smart Structure Technology
Last updated: 2020-02-09

## Slide 2
Edge Detection Applications
Crack detection
Augmented reality

## Slide 3
Edge Detection
Convert a 2D image into a set of curves
  Semantic and shape information
  More compact than pixels

## Slide 4
Origin of Edges
Surface normal discontinuity
Material discontinuity
Lighting discontinuity
Notes: https://www.pexels.com/photo/clear-glass-window-with-brown-and-white-wooden-frame-921294/

## Slide 5
Characterizing Edge by Differentiation
An edge is a place of rapid change in the image intensity function in a single direction.
Image
Intensity function
along a red line
First derivative
Edges correspond to extrema of derivative

## Slide 6
Image Derivatives
How can we differentiate a digital image ?
Option 1: Reconstruct a continuous image, f, then compute the derivative
Option 2: Take discrete derivative (finite difference)
pixel
How would you implement this as a kernel?

## Slide 7
Image Gradient
The gradient of an image:
The gradient points in the direction of most rapid increase in intensity
The gradient direction is given by
The edge strength is given by the gradient magnitude

## Slide 8
Example: Image Gradient

## Slide 9
Intensity Changes on an Image

## Slide 10
Intensity Changes on an Image (with Noise)

## Slide 11
Effects of Noise
Noisy input image
Where is the edge?

## Slide 12
(Review) Properties of Fourier Transforms
1. Time scaling
2. Time reversal
4. Time shifting
5. Modulation
Inverse spreading relationship
Only phase shift !
3. Differentiation
Sine wave

## Slide 13
Smoothing First and Applying a Derivative Operator

## Slide 14
Smoothing First and Applying a Derivative Operator (Continue)
Relationship with differentiation:
What is the advantage?

## Slide 15
2D Edge Detection Filter
Gaussian kernel
Derivative of Gaussian filter

## Slide 16
2D Edge Detection Filter (Continue)
-1 | 0 | 1
-1 | 0 | 1
-1 | 0 | 1
Prewitt operator
?

## Slide 17
Sobel Operator
Common approximation of derivative of Gaussian
-1 | 0 | 1
-2 | 0 | 2
-1 | 0 | 1
1 | 2 | 1
0 | 0 | 0
-1 | -2 | -1
The Sobel operator omits the 1/8 term because it does not make a difference for edge detection

## Slide 18
Sobel Operator (Example)

## Slide 19
Comparison of Derivative Operators (Prewitt and Sobel)

## Slide 20
Laplacian of Gaussian (1D Example)

## Slide 21
Laplacian of Gaussian
0 | -1 | 0
-1 | 4 | -1
0 | -1 | 0

## Slide 22
Implementation Issues for Gradient-based Edge Detection
The gradient magnitude is large along a thick “trail” or “ridge,” so how do we identify the actual edge points?
How do we link the edge points to form curves?

## Slide 23
Canny Edge Detector
This is probably the most widely used edge detector in computer vision
Theoretical model: step-edges corrupted by additive Gaussian noise
J. Canny, A Computational Approach To Edge Detection, IEEE Trans. Pattern Analysis and Machine Intelligence, 8:679-714, 1986.
Steps
Filter image with x, y derivatives of Gaussian
Find magnitude and orientation of gradient
Non-maximum suppression: Thin multi-pixel wide “ridges” down to single pixel width
Thresholding and linking (hysteresis): Define two thresholds: low and high and use the high threshold to start edge curves and the low threshold to continue them
MATLAB: edge(image, ‘canny’)

## Slide 24
Original Image and Its Gradient
original image (Lena)
X-Derivative of Gaussian
Y-Derivative of Gaussian
Gradient Magnitude

## Slide 25
Finding Edges

## Slide 26
Non-maximum Suppression
Check if pixel is local maximum along gradient direction
  Requires interpolating pixels p and r

## Slide 27
After Non-maximum Suppression

## Slide 28
Hysteresis Thresholding
Threshold at low/high levels to get weak/strong edge pixels
Do connected components, starting from strong edge pixels

## Slide 29
Final Canny Edges

## Slide 30
(Revisit) Effect of Gaussian Window Sizes

## Slide 31
Effect of σ (Gaussian Kernel Size)
The choice of  depends on desired behavior
  large  detects large scale edges
  small  detects fine features

## Slide 32
Effect of High and Low Thresholds
[0.4 0.8]
[0.4 0.5]
[0.2 0.5]
[0.1 0.5]

## Slide 33
Contour Detection and Image Segmentation Resources (Computer Vision Group in Berkeley)

## Slide 34
Hough Transform
The basic idea is to examine the parameter space for lines, rather than the image spaces.

## Slide 35
Image and Parameter Spaces
Equation of Line:
Find:
Consider point:
Image Space
Parameter Space
Parameter space also called Hough Space
Image Space
Parameter Space

## Slide 36
Line Detection by Hough Transform
Algorithm:
Quantize Parameter Space
Create Accumulator Array
Set
For each image edge increment:
If lies on the line:
Find local maxima in
Parameter Space
 | 1 |  |  |  |  |  | 1 |  | 
 |  | 1 |  |  |  | 1 |  |  | 
 |  |  | 1 |  | 1 |  |  |  | 
 |  |  |  | 2 |  |  |  |  | 
 |  |  | 1 |  | 1 |  |  |  | 
 |  | 1 |  |  |  | 1 |  |  | 
 | 1 |  |  |  |  |  | 1 |  | 

## Slide 37
Better Parameterization
NOTE:
Large Accumulator
More memory and computations
Improvement:
Line equation:
Here
Given points find
(Finite Accumulator Array Size)
Hough Space Sinusoid
Image Space
Hough Space
?

## Slide 38
Hough Transform Demo

## Slide 39
Example: Line Passing Through Three Dots
-70°
60°

## Slide 40
Example: Line Detection
1st Peak

## Slide 41
Mechanics of the Hough Transform
Difficulties
  how big should the cells be? (too big, and we merge quite different lines; too small, and noise causes lines to be missed)
How many lines?
  Count the peaks in the Hough array
  Treat adjacent peaks as a single peak
Which points belong to each line?
  Search for points close to the line
  Solve again for line and iterate

## Slide 42
Slide Credits and References
Lecture notes: S. Narasimhan
Lecture notes: Gordon Wetzstein
Lecture notes: Noah Snavely
Lecture notes: L. Fei-Fei
Lecture notes: D. Frosyth
Lecture notes: James Hayes
Lecture notes: Yacov Hel-Or